## Slide 1
2025. 09.
CARLO PINOKIO SIMULATOR USER MANUAL

## Slide 2
Ⅰ
User Hands-on

## Slide 3
PART ONE
1. User Hands-on
User Interface Overview
Installation Procedure
Hands-on Examples
Modeling Methodology

## Slide 4
Installation Procedure
4
1) Website Access
  http://www.carlo.co.kr/index.html

## Slide 5
Installation Procedure
5
2) Navigate to Download Page

## Slide 6
Installation Procedure
6
3) Base Download Process
1
2
  Click "PINOKIO BASE (Trial) Download" button
  Confirm download of potentially unverified file when prompted

## Slide 7
Installation Procedure
7
4) Simulator Download
  Download the ZIP file and extract it
  Open the Pinokio inst.msi file

## Slide 8
Installation Procedure
8
4) Simulator Download
  Run the msi file to start the installation
  Select the installation folder and click “Next” to proceed step by step until completion

## Slide 9
Installation Procedure
9
4) Simulator Download
  Go to the installation folder you set or C:\Carlo\Pinokio Simulator Setup folder
  Run the Pinokio.Install.exe file

## Slide 10
Installation Procedure
10
4) Simulator Download
  Run the PINOKIO installation program
  Select SIMULATOR
  Agree to the terms and conditions
  Select the installation folder

## Slide 11
Installation Procedure
11
4) Simulator Download
  Installation complete screen
  Create a shortcut icon / Select to run the program immediately after closing the installation program

## Slide 12
Installation Procedure
12
4) Simulator Download
  Run the PINOKIO Simulator

## Slide 13
PART ONE
1. User Hands-on
User Interface Overview
Installation Procedure
Hands-on Examples
Modeling Methodology

## Slide 14
UI Description
14
Overall UI Structure
Main Tab and Icons for Each Tab (Modeling/Simulation/Analysis/Window)
Node Addition/Deletion
and Node List Management
Node Attribute Information
3D Main View

## Slide 15
15
Modeling-Related UI
  Modeling Tab : This tab consolidates all functions related to modeling.
  New Button : Resets the interface to create a new model
  Load Button : Loads an existing model
  Save Button : Saves the current model in either DB or XML format
  Save As Button : Saves the current model under a different name in DB or XML format
  Edit Floor Button : Opens the interface for configuring floor-related settings
  Edit Product Button : Opens the interface for modifying product-related information
  Edit Step Button : Opens the interface for editing step-related configurations
  Edit Equipment Button : Opens the interface for modifying equipment-related details
  Make Random Commands Button : Generate random commands based on bay or port
1
2
3
4
5
6
7
8
9
10
UI Description
11
12
13
15
14
15
16
17

## Slide 16
Modeling-Related UI
  Edit ZCU Button : Feature to configure ZCUs and bays
  Edit Script Button : Opens the interface for editing scripts
  Edit Nodes Button : Opens the interface for batch editing properties of inserted nodes of the same type
  Edit Visible Button : Opens the interface to configure the visibility settings for inserted nodes of the same type
  Alignment Button : Aligns the selected nodes based on specified alignment options
  Initial Height Off/On Toggle : Button to toggle the Height column in the Insert Node section
  Coupled Model Off/On Toggle : Button to view only coupled nodes in the Node List
UI Description
16
16
16
1
2
3
4
5
6
7
8
9
10
11
12
13
16
14
15
16
17

## Slide 17
Simulation-Related UI
  Simulation Tab : Tab containing functions related to running simulations
  Animation Off/On Toggle : Button to enable or disable animation
  Animation Speed Spin/Bar : Spin control and scroll bar to adjust animation speed
  Background Dark/Light Toggle : Button to switch the MainView display between dark and light modes
  Auto Focusing Off/On Toggle : Button to enable or disable automatic tracking of the selected object every second
  Production/MHS Toggle : Button to switch to Production or MHS mode
  Run/Pause/Stop Button : Buttons to run, pause, or stop the simulation
  Reserve Pause Button : Button to open the screen for scheduling a simulation pause time
  Sim Start/End Time/Current Time Spin : Spin controls to set the simulation’s start and end times, and display the current simulation time
  Acceleration Rate Spin : Spin control to adjust the current simulation acceleration rate
UI Description
1
2
3
4
5
6
7
8
9
10
11
12
14
15
13

## Slide 18
18
Simulation-Related UI
  Warm Up Period : Button to set the simulation’s warm-up period
  Save Snapshot Button : Button to create a snapshot of the current simulation state (simulation must be paused)
  Load Snapshot Button : Button to load a snapshot file and resume the simulation from the saved point
  State-Based Colors Toggle : Button to change the colors of vehicles, equipment, and transport lines based on their states
  Python On Button : Button to Use Python
UI Description
1
2
3
4
5
6
7
8
9
10
11
12
14
15
13

## Slide 19
19
Analysis-Related UI
  Analysis Tab: Tab containing functions related to analysis
  Production Report Button: Button to open the production report screen
  AMHS Report Button: Button to open the logistics report screen
  Load Production Report Button: Button to load a previously saved production report screen
  Load AMHS Report Button: Button to load a previously saved logistics report screen
  ※ ②, ③ : Activated when the simulation starts
  ※ ④, ⑤ : Activated when the model is loaded (the production/logistics report file to be opened must match the loaded model)
1
2
3
4
5
UI Description

## Slide 20
20
Window-Related UI
  Window Tab: Tab containing functions to reopen various utility windows
  Insert Node Button: Button to reopen the window for selecting a node to insert
  Insert Coupled Model Button: Button to reopen the window for selecting a coupled model to insert
  Nodes Button: Button to reopen the window for managing the tree list of inserted nodes
  Object Properties Button: Button to reopen the window for viewing the properties of an object
  Reference Properties Button: Button to reopen the window for viewing the properties of a reference
1
2
3
4
5
6
UI Description

## Slide 21
UI Description
21
UI - Detail Description
Modeling – New
To initialize and create a new model
  Click the New Button
  Click Confirm to proceed
1
2

## Slide 22
22
UI - Detail Description
Modeling – Load
To load an existing model.
  Click the Load Button
  Select the model file to load and click it.
1
2
UI Description

## Slide 23
23
UI - Detail Description
Modeling – Save
To save the model.(db/xml)
  Click the Save Button
  For loaded models: Saves changes to the current file. For newly created models: Opens the Save As dialog to save the model under a new name.
1
UI Description
2

## Slide 24
24
UI - Detail Description
Modeling – Save As
To save the model under a different name(db/xml)
  Click the Save As Button
1
2
UI Description

## Slide 25
25
UI - Detail Description
Modeling – Edit Floor
To open the floor configuration screen
  Click the Edit Floor Button
  Configure floor settings (name, height, size, etc.)
  Add floors
  Delete the selected floor.
1
2
3
4
UI Description

## Slide 26
26
UI - Detail Description
Modeling – Edit Product
To open the product configuration screen
  Click the Edit Product Button
  Configure product settings.
  Configure product detail settings.
  Check details of product detail rows.
  Use the +/- Buttons to add or delete products.
1
2
3
5
4
UI Description

## Slide 27
27
UI - Detail Description
Modeling – Edit Product Detail
Reference Name – To configure the product type.
  Click Reference Name
  Set Product Type
1
2
UI Description

## Slide 28
28
UI - Detail Description
Modeling – Edit Product Detail
IDs of Step –Set Steps for Product
  Click IDs of Step
  All Step List configured in the model - Click the Step to configure - Drag and drop to ③
1
2
3
UI Description

## Slide 29
29
UI - Detail Description
Modeling – Edit Product Detail
Production Schedules –Set Schedules for Product
  Click Production Schedules
  Set Product Schedules - Creation Time : Time of creation - Interval Time : Interval between creations - Limit Time : Time when creation ends - Count : Number of generated products - Unit Value : Product capacity
  Set Production Schedules Detail
  Set Source Node for Product - Click Source Node(Please select a buffer or line) - Assign the Source Node for Product
  Click +/- Button to add or delete Schedules
1
2
3
4
5
UI Description

## Slide 30
30
UI - Detail Description
Modeling – Edit Step
Button to open the screen for modifying steps
  Click Edit Step Button
  Set Step
  Set Step detail
  Check details of Step detail Row
  Click +/- Button to add or delete Steps
1
2
3
5
4
UI Description

## Slide 31
31
UI - Detail 설명
1
UI Description
Modeling – Edit Step Detail
Step Type – Select the Type for the Step
  Select Step Type

## Slide 32
Modeling – Edit Step Detail
IDs of Eqp – Select the Eqp that performs the Step
  Click IDs of Eqp
  All Eqp List in the model - Check the Eqp that performs the Step
32
UI - Detail Description
1
UI Description
2

## Slide 33
Modeling – Edit Step Detail
Processing Time –Set details for Processing Time
  Click Processing Time
  Configure Distribution, Mean, and Offset
33
UI - Detail Description
1
UI Description
2

## Slide 34
Modeling – Edit Step Detail
Processing Unit – Select the Processing Type
  Click Processing Unit
  Select PART / UNIT / BATCH
34
UI - Detail Description
1
UI Description

## Slide 35
Modeling – Edit Step Detail
Cascading Interval Time – Set Interval Time for Cascading
  Enter Cascading Interval Time - Can be entered only when Processing Unit is UNIT or Part Type
35
UI - Detail Description
1
UI Description

## Slide 36
Modeling – Edit Step Detail
Processing Probability – Set the Probability for Processing
  Enter Processing Probability - If set to 0, it is equivalent to 100
36
UI - Detail Description
1
UI Description

## Slide 37
Modeling – Edit Step Detail
Sampling Probability – Set the Probability for Sampling
  Enter Sampling Probability - If set to 0, it is equivalent to 100
37
UI - Detail Description
1
UI Description

## Slide 38
Modeling – Edit Step Detail
Batch Min/Max –Set the minimum and maximum of the batch
  Enter Batch Minimum / Maximum Value - Execute the batch if the value is within the min and max range.
38
UI - Detail Description
1
UI Description

## Slide 39
39
UI - Detail Description
Modeling – Edit Step Detail
Input Products – Set Products entering the Step
  Click Input Products
  All Product List in the model - Click the Product to configure - Drag and drop to ③
1
2
3
UI Description
Output Products – Set Products exiting the Step
  Click Output Products
  All Product List in the model - Click the Product to configure - Drag and drop to ③
  - Can be configured only when Step Type is DEASSEMBLE or TRANSFORM

## Slide 40
40
UI - Detail Description
Modeling – Edit Equipment
Button to open the screen for modifying equipment
  Click Edit Equipment Button
  Set Equipment
  Set Equipment detail
1
2
3
UI Description

## Slide 41
41
UI - Detail Description
Modeling – Make Random Commands
Button to open the screen for making random commands
  Click Make Random Commands Button
  Set Command detail
1
2
3
UI Description

## Slide 42
42
UI - Detail Description
Modeling – Make Random Commands Detail
Button to open the screen for making random commands
  Run the simulation
  In AMHS Report, click the Traffic Volume tab.
  Set the Bay to Bay or Port to Port toggle, then click Search.
  Click the Export to Excel button to save the results in Excel format.
1
UI Description
2
3
4

## Slide 43
43
UI - Detail Description
Modeling – Make Random Commands Detail
Button to open the screen for making random commands
  Set the Sim Start/End Time and the number of commands to generate.
  Choose whether to generate by Bay to Bay or Port to Port. *Multiply is applied as a multiplier of the values entered in Excel.
  Import the Excel file exported from Traffic Volume in AMHS Report. *It is located inside the Traffic Volume KPI folder created in the Pinokio Simulator executable path.
  After finishing modifications to the generated data in the grid, apply the settings.
UI Description
1
2
3
4
5

## Slide 44
44
UI - Detail Description
Modeling – Edit ZCU
Button to open the screen for making ZCU or Bay (Zone)
  Click the Edit ZCU button.
  From Node list
  To Node list *Right-click a Line or Point to add it to the From/To nodes.
  List of lines belonging to the current Bay
  Select SubCS
  Select Bay or ZCU
  Add a new Bay or ZCU
  Delete a Bay or ZCU
  When From/To Nodes are set for a Bay, search the lines within the Bay based on those nodes.
  Delete the searched lines.
UI Description
1
2
3
4
7
8
9
10
5
6

## Slide 45
45
UI - Detail Description
Modeling – Edit Script
Button to open the screen for modifying scripts
  Click Edit Script Button
  All modifiable script list - Select the script to modify
  Edit the script in C# and save
1
2
3
UI Description

## Slide 46
46
UI - Detail Description
Modeling – Edit Nodes
Button to open the screen for bulk modifications of inserted nodes of the same type
  Click Edit Nodes Button
  Node Category List - Categories from the Insert Node Tab
  Node Type List - Node types of the selected category
  View all nodes inserted under the selected category/type - Click a row to locate the corresponding node on the main screen
  Editable Object Property List - Enter PropertyValue for items to be modified
  Check nodes to modify
  Click OK Button to apply bulk modifications
1
2
3
UI Description
4
5
6
7

## Slide 47
47
UI - Detail Description
Modeling – Edit Visible
Button to set the name/visibility of nodes
  Click Edit Visible Button
  Set Visible/Text
1
2
UI Description

## Slide 48
48
UI - Detail Description
Modeling – Alignment
Function to align selected nodes
  Click Alignment
  Select alignment type
1
2
UI Description

## Slide 49
49
UI - Detail Description
Simulation – Reserve Pause
Schedule a simulation pause time
  Click Reserve Pause Button
  Set Pause Time between Sim Now Time and Sim End Time
1
2
UI Description

## Slide 50
50
UI - Detail Description
Simulation – Snapshot
Function to configure a snapshot at a specific point
  Save SnapShot - Pause the simulation and click - Configure the snapshot for the current point - Create a snapshot file and reset the simulation
  Load SnapShot - Load the snapshot file and resume simulation from that point
1
UI Description
2

## Slide 51
51
UI - Detail Description
Simulation – State-Based Colors
Change node colors based on their state
  Vehicle - Color changes according to the vehicle's current state (IDLE, BUSY, etc.)
  Equipment - Color changes according to the equipment's current state (IDLE, BUSY, etc.)
  TransportLine - Color changes according to the congestion rate of the line
1
UI Description

## Slide 52
52
UI - Detail Description
Analysis – Production Report
Button to open the production report screen
  Click Production Report Button
  Open the Production Report window
  ※ Icon is activated after simulation starts
1
2
UI Description

## Slide 53
UI Description
53
UI - Detail Description
Analysis – Production Report Detail
  Step Trend - Check progress by step Eqp Operation Rate - Check equipment operation rate Factory Input / Output - Check the process flow
  Group By : - Select search group Select Targets : - Open the inquiry target window - Specify certain targets within the selected group Search : - View the report based on selected items
  Configure the search period/chart axis
1
2
3

## Slide 54
54
UI - Detail Description
Analysis – Production Report Detail
  Export the report as an Excel file
  Toggle chart data labels On/Off
  Export report charts
  Export report tables
1
2
3
4
UI Description

## Slide 55
UI Description
55
UI - Detail Description
Analysis – AMHS Report
Button to open the logistics report screen
  Click AMHS Report Button
  Open the AMHS Report window
  ※ Icon is activated after simulation starts
1
2

## Slide 56
UI Description
56
UI - Detail Description
Analysis – AMHS Report Detail
  MR Trend - Check Move Request CMD Trend - Check Command CMD Distribution - Check the time distribution of commands Vehicle Operation Rate - Check vehicle operation rate
  Start Target - Set the start point for Move Requests End Target - Set the end point for Move Requests Search - View the report based on selected items
  Configure the search period/chart axis
1
2
3

## Slide 57
UI Description
57
UI - Detail Description
Analysis – AMHS Report Detail
  Export the report as an Excel file
  Toggle chart data labels On/Off
  Export report charts
  Export report tables
1
2
3
4

## Slide 58
UI Description
58
UI - Detail Description
Analysis – AMHS Report Detail
  Traffic Volume - Check Command’s Source/Destination
  Control System - Select a system to search for commands Search - View the report based on selected items
  Configure the search period Bay To Bay / Port - Select which criteria to use when searching commands From / To Type - Filter From/To by name (contains)
1
2
3

## Slide 59
UI Description
59
UI - Detail Description
Analysis – AMHS Report Detail
  Total Commands Count
  Export report tables
  Command From/To Table - Columns: To / Rows: From
1
2
3

## Slide 60
UI Description
60
UI - Detail Description
Analysis – Load Production Report
Button to open a saved production report screen
  Click Load Production Report Button
  Select the report file from Bin/Debug/Simulation Results path
  ※ The report file must match the currently loaded model Confirm from SimResult_[Model Name] ※ Icon is activated only when a model is loaded
1
2

## Slide 61
UI Description
61
UI - Detail Description
Analysis – Load AMHS Report
Button to open a saved logistics report screen
  Click Load AMHS Report Button
  Select the report file from Bin/Debug/Simulation Results path
  ※ The report file must match the currently loaded model Confirm from SimResult_[Model Name] ※ Icon is activated only when a model is loaded
1
2

## Slide 62
PART ONE
1. User Hands-on
User Interface Overview
Installation Procedure
Hands-on Examples
Modeling Methodology

## Slide 63
Modeling Methodology
63
Node Insert
Node Insert
  Click Insert Node Tab
  Select the Node to add from the Tree List
  Check in the Nodes Tab
1
2
3

## Slide 64
Modeling Methodology
64
Node Insert
Node Insert – General Node
  Select Category – Node
  Add by a single left mouse click
1
2

## Slide 65
Modeling Methodology
65
Node Insert
Node Insert – Line Node
  Select Category – Line
  Set the start point by a left mouse click Move the mouse to the desired length Set the endpoint by another left mouse click
  ※ Holding the Shift Key while moving the mouse allows you to draw straight lines
1
2

## Slide 66
Modeling Methodology
66
Node Insert
Node Insert – Vehicle / Line Component Node
  Select Category – Vehicle / Line Component
  Move the mouse cursor over the line (the line color changes if the position is valid)
  Add by a single left mouse click
  ※ A warning message appears if it is not a line
1
2

## Slide 67
Modeling Methodology
67
Node Insert
Node Insert – Line Station Component Node
  Select Category – Line Station Component
  Move the mouse cursor over the line component (the line component color changes if the position is valid)
  Add by a single left mouse click
  ※ A warning message appears if it is not a line component
1
2

## Slide 68
Modeling Methodology
68
Coupled Model Insert
Coupled Model Insert
  Select the Coupled Model and click Add Button
  Check in the Nodes Tab
1
2

## Slide 69
Modeling Methodology
69
Node Layout Move
Node Layout Move – General Node
  Drag and drop by a single left mouse click
1

## Slide 70
Modeling Methodology
70
Node Layout Move
Node Layout Move – Line Node
  Change - Click one point and drag and drop
  Move - Click the line or select two points and the line, then drag and drop
1
2

## Slide 71
Modeling Methodology
71
Node Layout Move
Node Layout Move – Vehicle / Line Component Node
  Select with a left mouse click Drag and drop to the desired point on the line
1

## Slide 72
Modeling Methodology
72
Node Layout Move
Node Layout Move – Line Station Component Node
  Select with a left mouse click Drag and drop to the desired point on the line Component
1

## Slide 73
Modeling Methodology
73
Node Layout Move
Node Layout Move – Coupled Model
  Select from the tree with a left mouse click Drag and drop to the desired point of the Coupled Model ※ Moving a Coupled Model also moves all its sub-nodes
1

## Slide 74
Modeling Methodology
74
Node Hierarchy Move
Node Hierarchy Move
  Click one row (Node) in the tree to move
  Select one of Line / Line Station / Vehicle Drag and drop into the SubCS
  ※ All nodes in the connected network are moved together
1
2

## Slide 75
Modeling Methodology
75
Node Delete
Node Delete
  Click one row (Node) in the tree and press the Delete Key
  Click in the Main View with a left mouse click and press the Delete Key
1
2

## Slide 76
Modeling Methodology
76
Modeling Undo/Redo
Node Modeling Undo / Redo
  Undo - Ctrl + Z - Remove the created node
  Redo - Ctrl + Shift + Z or Ctrl + Y - Restore the removed node
1
2

## Slide 77
PART ONE
1. User Hands-on
User Interface Overview
Installation Procedure
Hands-on Examples
Modeling Methodology

## Slide 78
Hands-on Examples
78
Fab Model

## Slide 79
Hands-on Examples
79
OHT Line & OHT
  Select OHTLine from Insert Node Tab
  Left-click the mouse to specify the Start Point of the OHT Line, then left-click again to specify the End Point and create the OHT Line
  Select OHT from Insert Node Tab
  Left-click on a point on the OHT Line to create an OHT

## Slide 80
Hands-on Examples
80
OHT Lines
  Select OHTLine from Insert Node Tab
  The Start Point of the next OHT Line is specified by left-clicking the End Point of the previously drawn OHT Line then Left-click again to finalize the End Point and create the OHT Line. * For a CurvedLine, the angle is calculated and generated automatically

## Slide 81
Hands-on Examples
81
Copy & Paste
  Drag to select the OHT Lines and copy them using Ctrl+C
  Paste them at the desired location with Ctrl+V

## Slide 82
Hands-on Examples
82
Bays
  Create three InterBays by creating OHT Lines, and add two Bridges to connect the IntraBays.

## Slide 83
Hands-on Examples
83
OCS
  Select the Insert Coupled Model tab.
  Choose OCS (OHT Control System).
  Click Add to insert an OCS SubCS.
  Drag and select all three IntraBays and two InterBays.
  From the Nodes window, drag the nodes marked in gray into the OCS.

## Slide 84
Hands-on Examples
84
Equipment
  In the Insert Node tab, click the Ref Type ComboBox under Equipment and select the desired Equipment. *SizableBox creates a rectangular Equipment in the size you specify.
  Left-click at the desired location to add the Equipment.

## Slide 85
Hands-on Examples
85
LineStation & EQP Port
  In the Insert Node tab, select OHTLineStation.
  Click on the desired position along the OHT Line to create a LineStation.
  Select UTB (Under Track Buffer).
  Left-click at the LineStation position to create the UTB.

## Slide 86
Hands-on Examples
86
LineStation & EQP Port
  Select UTB, and in the Object Properties panel on the right, set Port to True. *This is to use it as the In/Out Port of the Equipment.

## Slide 87
Hands-on Examples
87
Link
  In the Insert Node tab, select Link.
  Left-click sequentially to specify the start node and the end node of the Link. *In this example, it represents the In/Out Ports of the Equipment.

## Slide 88
Hands-on Examples
88
Side Track Buffer
  In the Insert Node tab, select STB.
  Left-click at the LineStation position to create the UTB.

## Slide 89
Hands-on Examples
89
Bay Setting
  Click the Edit Zone icon and select a Bay.
  Click the Add button to create a new Bay.
  Set the name of the Bay.
  Right-click on the Line corresponding to the Bay’s entry point and select Add From Node. Right-click on the Line corresponding to the Bay’s exit point and select Add To Node. *The From Node is displayed in red, and the To Node is displayed in green.
  Click Explore the Area to scan all the Lines within the Bay.

## Slide 90
Hands-on Examples
90
ZCU Setting
  Click the Edit Zone icon and select a ZCU.
  Click the Add button to create a new ZCU.
  Set the name of the ZCU.
  Right-click on the Point corresponding to the ZCU’s entry point and select Add From Node. Right-click on the Point corresponding to the ZCU’s exit point and select Add To Node. *The From Node is displayed in red, and the To Node is displayed in green.
  Click Explore the Area to scan all the Lines within the ZCU.

## Slide 91
Hands-on Examples
91
Edit Step
  Click the Edit Step icon to configure a Step.
  Click the + button to add a new Step.
  Click ProcessingTime to set the Processing Time.

## Slide 92
Hands-on Examples
92
Edit Step
  Click Ids of EQP to select the Equipment that will perform the Step.
  Select the Equipment by clicking the corresponding checkboxes.

## Slide 93
Hands-on Examples
93
Edit Product
  Click the Edit Product icon to configure a Product.
  Click the + button to add a new Product.
  Click Ids of Step to select the Steps that the Product will perform.
  Drag the selected Steps from the panel on the right and drop them into the grid on the left.

## Slide 94
Hands-on Examples
94
Edit Product
  Click Production Schedules to create a Product input plan.
  Click Source Node to set the node where the Product will be introduced.
  Select the Source Node for Product input.
  Set the Creation Time, Interval Time, and other parameters.